## Slide 1: Platform for Microrobot Navigation
Nafiseh Vahabi
MRes

## Slide 2: Motivation
Benefit of robotic surgery over invasive surgery
  Shorter hospitalization
  Reduced pain and discomfort
  Minimal scarring
Miniaturization
  Cardiovascular surgery

## Slide 3: History of Swimming Microrobot
At 1930 (Bruce) first swimming mechanism at micro scale
Bell 2007 first Artificial Bacteria Flagellum
Zhang 2009, characterized them
Mahoney et al. 2012, velocity control
Nelson et al. 2013, actuation and fabrication

## Slide 4: Potential Application
application divided into two categories:
  Biomedical In vivo
    Minimally invasive procedures
    Targeted drag delivery
    Ablation of the material
    Delivery of hyperthermia for cancer treatment
  In vitro (lab-on-a-chip)
    Manipulation and characterization of cells
    Microfluidic control
Most of these applications placed micro-device into fluidic or soft environment.

## Slide 5: Key Challenges
Design a helical microrobot and characterization
Evaluation of nano printed structures
Analysis of locomotion swimming helical microrobot in high viscous fluid
Analysis of magnetically actuated helix
Try simulator packages,

## Slide 6: Project Overview
  Simulation
Fabrication
Design
Validation
Propulsion Algorithm
Actuation Algorithm
Nanoscribe
SEM
Optimization

## Slide 7: Design
Why helical shape?
  Non-reciprocal configuration
  Net motion
  Helix has a same angle of
  attack to the direction of motion

## Slide 8: Design
Helix key parameters
    Helix length
    Pitch
    Pitch angle
    Helix radius
    Filament radius

## Slide 9: Simulation
Desired
Velocity
Propulsion
Algorithm
Actuation
Algorithm
Torque
Magnetic
Field
Electric
Current
RFT
RSM
BST

## Slide 10: Propulsion Modeling
Resistive Force Theory (RFT)
  Decomposes the velocity vector
  Relate them to drag force
  Define the coordinate frame for helix
  Rotate from segment frame to helix frame
  Express the differential relating velocity to force in three dimension
  Velocity of segment decomposes to the sum of rotational and translational velocity

## Slide 11: Resistive Force Theory
Relating fluidic force and torque to the translational and rotational velocity

## Slide 12: Propulsion Modeling
Regular Stokeslet Methods (RSM)
  Discretizes the surface of helix filament
  Represent each surface
  element by regularized
  stokeslet.
Body Slender Theory (BST)
  Using stokeslet and
  doublets arranged along the
  Helical centre line.

## Slide 13: Actuation
Applied magnetic field
To compensate the drift caused by the weight
  Direction that it must point
  Rotational velocity
Find the desired velocity from propulsion equations system
Convert the velocity from helix frame to the world frame
Decompose the velocity to vertical and horizantal vectors

## Slide 14: Actuation
If
If

## Slide 15: Simulation Algorithm

## Slide 16: Fabrication
Nanoscribe
SEM
Coating
Magnetic
Material
Preparing
Production
Post-processing
Sputter Coating
Image Analysis

## Slide 17: Nanoscribe

## Slide 18: Scanning Electron Microscope
Sputter Coating

## Slide 19: Results
Simulation results
    Simulation framework
    Linear relationship between rotational and translational velocity
    Linear relationship between translational velocity and electric current
Design result
  Variable pitch helical design
Fabrication results
  Fabricating different design of microrobot

## Slide 20: Simulation Result

## Slide 21: Simulation Result

## Slide 22: Simulation Result

## Slide 24: Design Results
- Helix with the variable pitch
- Capable to add propellers

## Slide 25: Fabrication Result

## Slide 26: My Contribution
The helix design with a variable pitch
The first application of Regularized Stokeslet Method and Body
Slender Theory in remotely controlled swimming microrobot to model the propulsion of the microrobot in high viscous fluid.

## Slide 27: Conclusion
Mathematics model to find electric current from microrobot velocity is solved
New design of microrobot to satisfy fabrication requirement
Helix propulsion methods for remotely controlled microrobot
Basic framework for microrobot simulation
Future work
  Optimizing simulation platform
  Applying new actuation method such as ultrasonic
  Designing propeller with the helix tail
  Validation

## Slide 28: Thank you for your attention Thanks to my supervisors Prof. Guang-Zhong Yang Dr. Vincenzo Curto Dr. Henry Ip